## Slide 1
Arduino Structure and Design
Part 1

## Slide 5
micro controller unit
MCU

## Slide 6
ARDUINO UNO REV3
Code: A000066

## Slide 7
ARDUINO UNO REV3
Code: A000066
Microcontroller | ATmega328P
Operating Voltage | 5V
Input Voltage (recommended) | 7-12V
Input Voltage (limit) | 6-20V
Digital I/O Pins | 14 (of which 6 provide PWM output)
PWM Digital I/O Pins | 6
Analog Input Pins | 6
DC Current per I/O Pin | 20 mA
DC Current for 3.3V Pin | 50 mA
Flash Memory | 32 KB (ATmega328P) of which 0.5 KB used by bootloader
SRAM | 2 KB (ATmega328P)
EEPROM | 1 KB (ATmega328P)
Clock Speed | 16 MHz
LED_BUILTIN | 13
Length | 68.6 mm
Width | 53.4 mm
Weight | 25 g

## Slide 8
ARDUINO NANO
Code: A000005

## Slide 9
ARDUINO NANO
Code: A000005
Microcontroller | ATmega328
Architecture | AVR
Operating Voltage | 5 V
Flash Memory | 32 KB of which 2 KB used by bootloader
SRAM | 2 KB
Clock Speed | 16 MHz
Analog IN Pins | 8
EEPROM | 1 KB
DC Current per I/O Pins | 40 mA (I/O Pins)
Input Voltage | 7-12 V
Digital I/O Pins | 22 (6 of which are PWM)
PWM Output | 6
Power Consumption | 19 mA
PCB Size | 18 x 45 mm
Weight | 7 g
Product Code | A000005

## Slide 10
ARDUINO MICRO
Code: A000053

## Slide 11
ARDUINO MINI 05
Code: A000087

## Slide 12
ARDUINO MEGA 2560 REV3
Code: A000067

## Slide 13
ARDUINO MEGA 2560 REV3
Code: A000067
Microcontroller | ATmega2560
Operating Voltage | 5V
Input Voltage (recommended) | 7-12V
Input Voltage (limit) | 6-20V
Digital I/O Pins | 54 (of which 15 provide PWM output)
Analog Input Pins | 16
DC Current per I/O Pin | 20 mA
DC Current for 3.3V Pin | 50 mA
Flash Memory | 256 KB of which 8 KB used by bootloader
SRAM | 8 KB
EEPROM | 4 KB
Clock Speed | 16 MHz
LED_BUILTIN | 13
Length | 101.52 mm
Width | 53.3 mm
Weight | 37 g

## Slide 14
ARDUINO DUE
Code: A000062

## Slide 15
www.Arduino.cc

## Slide 16
Arduino Sketch
Arduino IDE

## Slide 17
#include <iostream>
using namespace std;
int main() { … }
CODE (.cpp)
C++ Compile
compiler
4d5a 9000 0300 0000 0400 0000 ffff 0000
b800 0000 0000 0000 4000 0000 0000 0000
0000 0000 0000 0000 0000 0000 0000 0000
0000 0000 0000 0000 0000 0000 d800 0000
0e1f ba0e 00b4 09cd 21b8 014c cd21 5468
6973 2070 726f 6772 616d 2063 616e 6e6f
7420 6265 2072 756e 2069 6e20 444f 5320
6d6f 6465 2e0d 0d0a 2400 0000 0000 0000
31b8 843a 75d9 ea69 75d9 ea69 75d9 ea69
b6d6 b569 77d9 ea69 75d9 eb69 eed9 ea69
b6d6 b769 64d9 ea69 21fa da69 7fd9 ea69
b2df ec69 74d9 ea69 5269 6368 75d9 ea69
0000 0000 0000 0000 0000 0000 0000 0000
0000 0000 0000 0000 5045 0000 4c01 0500
c1e3 1a4b 0000 0000 0000 0000 e000 0f01
0b01 0600 005a 0000 00d4 0100 0004 0000
cb30 0000 0010 0000 0070 0000 0000 4000
0010 0000 0002 0000 0400 0000 0600 0000
0400 0000 0000 0000 0000 0600 0004 0000
0000 0000 0200 0080 0000 1000 0010 0000
0000 1000 0010 0000 0000 0000 1000 0000
0000 0000 0000 0000 a473 0000 b400 0000
0020 0400 60d5 0100 0000 0000 0000 0000
0000 0000 0000 0000 0000 0000 0000 0000
0000 0000 0000 0000 0000 0000 0000 0000
0000 0000 0000 0000 0000 0000 0000 0000
0000 0000 0000 0000 0000 0000 0000 0000
Machine Language

## Slide 18
4d5a 9000 0300 0000 0400 0000 ffff 0000
b800 0000 0000 0000 4000 0000 0000 0000
0000 0000 0000 0000 0000 0000 0000 0000
0000 0000 0000 0000 0000 0000 d800 0000
0e1f ba0e 00b4 09cd 21b8 014c cd21 5468
6973 2070 726f 6772 616d 2063 616e 6e6f
7420 6265 2072 756e 2069 6e20 444f 5320
6d6f 6465 2e0d 0d0a 2400 0000 0000 0000
31b8 843a 75d9 ea69 75d9 ea69 75d9 ea69
b6d6 b569 77d9 ea69 75d9 eb69 eed9 ea69
b6d6 b769 64d9 ea69 21fa da69 7fd9 ea69
b2df ec69 74d9 ea69 5269 6368 75d9 ea69
0000 0000 0000 0000 0000 0000 0000 0000
0000 0000 0000 0000 5045 0000 4c01 0500
c1e3 1a4b 0000 0000 0000 0000 e000 0f01
0b01 0600 005a 0000 00d4 0100 0004 0000
cb30 0000 0010 0000 0070 0000 0000 4000
0010 0000 0002 0000 0400 0000 0600 0000
0400 0000 0000 0000 0000 0600 0004 0000
0000 0000 0200 0080 0000 1000 0010 0000
0000 1000 0010 0000 0000 0000 1000 0000
0000 0000 0000 0000 a473 0000 b400 0000
0020 0400 60d5 0100 0000 0000 0000 0000
0000 0000 0000 0000 0000 0000 0000 0000
0000 0000 0000 0000 0000 0000 0000 0000
0000 0000 0000 0000 0000 0000 0000 0000
0000 0000 0000 0000 0000 0000 0000 0000
Machine Language

## Slide 19
4d5a 9000 0300 0000 0400 0000 ffff 0000
b800 0000 0000 0000 4000 0000 0000 0000
0000 0000 0000 0000 0000 0000 0000 0000
0000 0000 0000 0000 0000 0000 d800 0000
0e1f ba0e 00b4 09cd 21b8 014c cd21 5468
6973 2070 726f 6772 616d 2063 616e 6e6f
7420 6265 2072 756e 2069 6e20 444f 5320
6d6f 6465 2e0d 0d0a 2400 0000 0000 0000
31b8 843a 75d9 ea69 75d9 ea69 75d9 ea69
b6d6 b569 77d9 ea69 75d9 eb69 eed9 ea69
b6d6 b769 64d9 ea69 21fa da69 7fd9 ea69
b2df ec69 74d9 ea69 5269 6368 75d9 ea69
0000 0000 0000 0000 0000 0000 0000 0000
0000 0000 0000 0000 5045 0000 4c01 0500
c1e3 1a4b 0000 0000 0000 0000 e000 0f01
0b01 0600 005a 0000 00d4 0100 0004 0000
cb30 0000 0010 0000 0070 0000 0000 4000
0010 0000 0002 0000 0400 0000 0600 0000
0400 0000 0000 0000 0000 0600 0004 0000
0000 0000 0200 0080 0000 1000 0010 0000
0000 1000 0010 0000 0000 0000 1000 0000
0000 0000 0000 0000 a473 0000 b400 0000
0020 0400 60d5 0100 0000 0000 0000 0000
0000 0000 0000 0000 0000 0000 0000 0000
0000 0000 0000 0000 0000 0000 0000 0000
0000 0000 0000 0000 0000 0000 0000 0000
0000 0000 0000 0000 0000 0000 0000 0000

## Slide 20
The C++ Programming Language

## Slide 22
I/O Pin

## Slide 23
Analog vs Digital

## Slide 24
LED Control

## Slide 25
.ino
// the setup function funs once when you press reset or power the board
void setup() {
// initialize digital pin 13 as on output
pinMode(13, OUTPUT);
}
// the loop function runs over and over again forever
void loop() {
digitalWrite(13, HIGH); // turns the LED on (HIGH is the voltage level)
delay(1000); // wait for a second
digitalWrite(13, LOW); // turn the LED off by making the voltage LOW
delay(1000); // wait for a second
}

## Slide 27
PWM
Pulse Width Modulation

## Slide 30
.ino
void setup() {
pinMode(3, OUTPUT);
}
void loop() {
for (int i=0; i<255; i++) {
analogWrite(3, i);
delay(100);
}
for (int i=255; i>0; i--) {
analogWrite(3, i);
delay(100);
}
}

## Slide 33
Breadboard

## Slide 36
Vcc
GND

## Slide 37
Sensor Connection

## Slide 39
.ino
void setup() {
pinMode(3, INPUT_PULLUP);
Serial.begin(9600);
}
void loop() {
Serial.print(‘[DHT11 SENSOR] ’);
Serial.println(analogRead(3));
}
void setup() {
Serial.begin(9600);
}
void loop() {
Serial.print(‘[DHT11 SENSOR] ’);
Serial.println(analogRead(A1));
}
Digital Pin
Analog Pin

## Slide 41
Motor Connection

## Slide 42
Servo Motor
DC Motor

## Slide 45
.ino
#include <Servo.h>
Servo motor;
void setup() {
motor.attach(3);
}
void loop() {
for (int i=0; i<180; i++) {
motor.write(i);
delay(100);
}
for (int i=180; i>0; i--) {
motor.write(i);
delay(100);
}
}

## Slide 49
.ino
void setup() {
pinMode(3, OUTPUT);
}
void loop() {
for (int i=0; i<255; i++) {
analogWrite(3, i);
delay(100);
}
for (int i=255; i>0; i--) {
analogWrite(3, i);
delay(100);
}
}
void setup() {
pinMode(3, OUTPUT);
}
void loop() {
digitalWrite(3, HIGH);
}
digitalWrite
PWM - analogWrite

## Slide 51
Push Button Connection

## Slide 53
.ino
void setup() {
pinMode(2, INPUT_PULLUP);
pinMode(13, OUTPUT);
}
void loop() {
if (digitalRead(2) == HIGH) {
digitalWrite(13, HIGH);
} else {
digitalWrite(13, LOW);
}
}

## Slide 55
문제가 발생했을 때

## Slide 56
“말은 쉽지, 코드를 보여줘.” ”Talk is cheap. Show me the code.”
- Linux Torvalds

## Slide 57
Arduino Structure and Design
Part 2

## Slide 58
I/O Pins

## Slide 63
The C++ Programming Language

## Slide 64
.ino
// the setup function funs once when you press reset or power the board
void setup() {
// initialize digital pin 13 as on output
pinMode(13, OUTPUT);
}
// the loop function runs over and over again forever
void loop() {
digitalWrite(13, HIGH); // turns the LED on (HIGH is the voltage level)
delay(1000); // wait for a second
digitalWrite(13, OUTPUT); // turn the LED off by making the voltage LOW
delay(1000); // wait for a second
}

## Slide 65
function

## Slide 66
PWM
Pulse Width Modulation

## Slide 70
h bridge 회로

## Slide 71
analogWrite();
int r = analogRead();

## Slide 72
Serial communication

## Slide 74
Arduino IDE Install
Coming soon …

## Slide 75
S4A Install

## Slide 76
http://s4a.cat/